## Slide 1
IDS 552
Guest Instructor: Parshan Pakiman
Warehouse Management

## Slide 2: Discussion outline
Warehousing in online retailing
Warehousing basics
Decisions:
  How to select equipment and technology
  How to store products
  How to pick and ship products (next class)

## Slide 3: Logistics of online retailing
e-Commerce
Logistics

## Slide 4: Supply chain of online retailing
Suppliers
Regional Warehouses
Local Fulfillment Centers
Consumers

## Slide 5: Offline and online demand
The difference between fulfilment for offline and online demands
Fulfillment for offline demands:
  Ship products to retail stores
  Smaller number of orders
  Large quantity for each order
Fulfillment for online demands:
  Ship products to end consumers
  Large number of orders
  Small quantity for each order

## Slide 6
Warehousing basics

## Slide 7: Types of warehouses
Retail distribution center
Service parts distribution center
E-commerce distribution center (fulfillment center)
3rd Party Logistic (3PL) warehouse
Perishable warehouse
Notes: A retail distribution center typically supplies product to retail stores, such as Wal-Mart or Target. The immediate customer of the distribution center is a retail store, which is likely to be a regular or even captive customer, receiving shipments on regularly scheduled days.
Service parts distribution center: They hold spare parts for expensive capital equipment, such as automobiles, airplanes, computer systems, or medical equipment. Because of the large number of parts, total activity in the DC may be statistically predictable, but the demand for any particular part is relatively small and therefore hard to predict. This means that the variance of demand can
be large and so relatively large quantities of safety stock must be held. These skus require much space. This in turn increases travel distances and makes order-picking less efficient.
E-commerce distribution center typically receives small orders from individuals by phone, fax, or the Internet. Orders are typically small, for only 1–3 items, but there may be many such orders, and they are to be filled and shipped immediately after receipt. Because customer orders require instant response, such distributors typically try to shape demand by offering special prices for ordering at certain times or in certain quantities or for accepting more variable delivery dates.
A 3PL warehouse is one to which a company might outsource its warehousing operations. thereby gaining economies of scale.
A perishables warehouse may handle food, fresh flowers, vaccines, or other product requiring refrigeration to protect its very short shelf life. Such DCs are distinctive in that product dwells within for very short times, frequently only hours. Also, there is a great emphasis on using space effectively because, with refrigeration, it is so expensive. They face many challenges in inventory management, including requirements to ship product according to FIFO (First-In-First-Out) or FEFO (First-Expired-First-Out). Also, there are typically many restrictions on how product is handled.

## Slide 8: Units of handling
Notes: A stock keeping unit, or SKU, is the smallest physical unit of a product that is tracked by an organization. Upstream in the supply chain, product generally flows in larger units, such as pallets; and is successively broken down into smaller units as it moves downstream, as
suggested in Figure 2.2. Thus a product might move out of the factory and to regional distribution centers in pallet-loads; and then to local warehouses in cases; and finally to retail stores in inner-packs or even individual pieces, which are the smallest units offered to the consumer.

## Slide 9: Warehouse operations
Receiving
Shipping
Put-away
Checking & packing
Order-picking
Pallet picking
Case picking
Piece picking
Order-picking costs about 55% of the total operating expense.
Within order-picking, traveling is the most time-consuming.

## Slide 10: How to fulfill orders?
How to select equipment and technology
How to store products
How to pick and ship products

## Slide 11
Scenario 1:
Pallet
Scenario 2:
Carton
Scenario 3:
Piece
When does each of these scenarios occur?

## Slide 12: Storage equipment
Pallet or case picking
  Pallet racks
    Bulk storage
Piece picking
  Bin-shelving
    Slower-moving items
  Gravity flow racks
    Faster-moving items

## Slide 13: Single-deep racks
  Easily accessible, require more aisle space

## Slide 14: Pallet flow racks
Shelves are tilted with rollers
Picking and restocking are performed from different aisles
For high throughput skus

## Slide 15: Bin-shelving

## Slide 16: Bin-shelving
Shallow shelves
Both picking and restocking must be done from the pick face
Suitable for slower-moving skus

## Slide 17: Gravity flow rack

## Slide 18: Gravity flow rack

## Slide 19: Gravity Flow Rack with a pick-to-light system

## Slide 20: Gravity Flow Rack with a pick-to-light system

## Slide 21: Gravity flow rack
Tilted and deep shelves
One case of a product on the pick face
High sku density
Some are supported by a pick-to-light system
Restock from the back
Suitable for faster-moving skus

## Slide 22: Handling equipment
Turret Truck (Forklift)
Order-Picker Truck
AS/RS
Conveyor
Notes: automated storage and retrieval systems (AS/RS)

## Slide 23: Turret truck
For very narrow aisles (5 to 7 feet)

## Slide 24: Order-picker trucks

## Slide 25: Automated storage and retrieval system (AS/RS)
https://www.youtube.com/watch?v=kdVet_UOx30&feature=related

## Slide 26: Automated storage and retrieval system (AS/RS)

## Slide 27: Conveyors
https://www.youtube.com/watch?v=KgpE1q9s9O0

## Slide 28: Conveyors

## Slide 29: Conveyors
Change the economics of travel
Partition a warehouse into zones
  Create problems of balancing work among zones
Store conveyable product far from shipping
Store non-conveyable product close to shipping

## Slide 30: Other technologies
High-density storage systems
  https://www.youtube.com/watch?v=iyVDMp2bL9c
Kiva robots
  https://www.youtube.com/watch?v=UtBa9yVZBJM
Amazon’s drones
  https://www.youtube.com/watch?v=Le46ERPMlWU
Meijer automation
  https://www.youtube.com/watch?v=bn5jjVKhFUs

## Slide 31: How to fulfill customer orders?
How to select equipment and technology
How to store products
How to pick and ship products

## Slide 32: Fast-pick area
Reserve
Fast-pick area
Restock
Pick
Pick

## Slide 33: Fast-pick area (bottom of rack)

## Slide 34: Fast-pick area (pallet flow rack)

## Slide 35: Fast-pick area (gravity flow rack)

## Slide 36: Summary
How to fulfill customer orders?
  How to select equipment and technology?
    Pallet racks for pallets
    Bin-shelving for slower-moving items
    Gravity flow racks for faster-moving items
  How to store products?
    Use fast-pick areas to reduce response time
  How to pick and ship products?

## Slide 37: Logistics of online retailing

## Slide 38: Logistics of online retailing

## Slide 39: When and how much to order from each supplier?
Suppliers
Regional Warehouses
Local Fulfillment Centers
Consumers
Decision 1

## Slide 40: How much to store in each warehouse for each product?
Suppliers
Regional Warehouses
Local Fulfillment Centers
Consumers
Decision 2

## Slide 41: Which warehouse to retrieve from?
Suppliers
Regional Warehouses
Local Fulfillment Centers
Consumers
Decision 3

## Slide 42: How to fulfill customer orders?
Suppliers
Regional Warehouses
Local Fulfillment Centers
Consumers
Decision 4

## Slide 43: Sample pick list
Pick line